## Slide 1: Selection of Sensors for Efficient Transmitter Localization
Arani Bhattacharya, Caitao Zhan, Himanshu Gupta, Samir R. Das, Petar M. Djuric
Notes: Good afternoon everyone. I am Arani Bhattacharya of Stony Brook University, and I would like to present out work “A First Look at Performance of TV Streaming Sticks”.

## Slide 2: Rising Threat of Unauthorized Transmission
Intruder (Unauthorized transmitter)
?
How can we monitor spectrum?
Notes: With the arrival of smart TVs, streaming sticks are used to stream movies and other videos over the Internet. These sticks have the form factor of a dongle and they are plugged into the HDMI port of TVs. There are three TV streaming sticks that are commonly available in the US market – Amazon Fire, Chromecast and Roku. A key question of active interest for users is the difference among these devices.

## Slide 3: A Distributed Spectrum Monitoring System
Fusion Center
Location of Unauthorized Transmission
Spectrum
sensors
?
Deploy large number of cheap but noisy spectrum sensors;
utilize robust localization to reduce impact of noise
Notes: With the arrival of smart TVs, streaming sticks are used to stream movies and other videos over the Internet. These sticks have the form factor of a dongle and they are plugged into the HDMI port of TVs. There are three TV streaming sticks that are commonly available in the US market – Amazon Fire, Chromecast and Roku. A key question of active interest for users is the difference among these devices.

## Slide 4: Running Sensors has a Recurring Cost
Fusion Center
May have limited energy
Cost of data transmission
Location of Unauthorized Transmission
Notes: With the arrival of smart TVs, streaming sticks are used to stream movies and other videos over the Internet. These sticks have the form factor of a dongle and they are plugged into the HDMI port of TVs. There are three TV streaming sticks that are commonly available in the US market – Amazon Fire, Chromecast and Roku. A key question of active interest for users is the difference among these devices.

## Slide 5: We Focus on Sensor Selection
Fusion Center
Select sensors
Location of Unauthorized Transmission
Relevant sensors
Budget
$$$
Select the most relevant sensors to localize
unauthorized transmission
Notes: With the arrival of smart TVs, streaming sticks are used to stream movies and other videos over the Internet. These sticks have the form factor of a dongle and they are plugged into the HDMI port of TVs. There are three TV streaming sticks that are commonly available in the US market – Amazon Fire, Chromecast and Roku. A key question of active interest for users is the difference among these devices.

## Slide 6: Content
Motivation of Sensor Selection
Problem Formulation
Our Algorithm
Evaluation

## Slide 7: Sensor Selection: Optimization Problem
Max Accuracy subject to: # Sensors ≤ Budget
Need to define accuracy of localization
?
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 8: Localization is a form of Hypothesis Classification
Select sensors
?
Distribution of Location L1
Distribution of Location L2
Well-known for providing the optimal accuracy
Classify data point using a threshold.
Threshold value given by Maximum a Posteriori Estimate
Sensing Metric
Known a priori by training
Notes: With the arrival of smart TVs, streaming sticks are used to stream movies and other videos over the Internet. These sticks have the form factor of a dongle and they are plugged into the HDMI port of TVs. There are three TV streaming sticks that are commonly available in the US market – Amazon Fire, Chromecast and Roku. A key question of active interest for users is the difference among these devices.

## Slide 9: Maximum a Posteriori Estimate in a Realistic Setting
L1
L2
L3
Divide entire area into grid cells
?
Lm
Collect training data corresponding to each grid cell
P(Xi | Li) = Data if intruder is at Li = Known by training
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 10: Maximum a Posteriori Estimate in a Realistic Setting
P(L1)
P(L2)
P(L3)
Divide entire area into grid cells
Compute probability of intruder at each location by Bayes rule
?
P(Lm)
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 11: Maximum a Posteriori Estimate in a Realistic Setting
Divide entire area into grid cells
Compute probability of intruder at each location by Bayes rule
Select maximum
?
P(Lm)
L1
L3
L2
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 12: Can we define accuracy of MAP?
P(MAP = 1 | L1)
L2
L3
Lm
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 13: Can we define accuracy of MAP?
P(MAP = 1 | L1)
P(MAP = 2 | L2)
L1
L3
Lm
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 14: Accuracy of MAP: Probability of MAP giving right location
Expected Accuracy =
P(MAP = 1 | L1)
P(MAP = 2 | L2)
.
.
.
P(MAP = m | Lm)
L2
L3
L1
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 15: Sensor Selection: Optimization Problem
L2
L3
L1
Lm
Max Accuracy subject to: # Sensors ≤ Budget
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 16: Sensor Selection as an Optimization Problem
NP-Hard Problem; variant of stochastic set cover.
Our goal is to find an approximate solution
Maxsubject to:
T = sensor subset; S = available sensors; B = budget
L2
L3
L1
Lm
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 17: Content
Motivation of Sensor Selection
Problem Formulation
Our Algorithm
Evaluation

## Slide 18: A “Greedy” Algorithm
“Monotone”:
No sensor has a negative gain
“Submodular”:
Gains follow law of diminishing returns
Size of subset
Accuracy of Localization
Size of subset
Accuracy of Detection
Start with empty subset ,
i.e.
For all available sensors , compute gain and select the one with highest gain
Return selected sensors
Budget reached?
No
Approximation factor of 1 – 1/e,
subject to conditions
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 19: Two Key Conditions on Objective Function
Monotone submodular objectives have approximation results using greedy algorithm
“Monotone”:
No sensor has a negative gain
“Submodular”:
Gains follow law of diminishing returns
Size of subset
Accuracy of Localization
Size of subset
Accuracy of Localization
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 20: Case of Two Locations
“Monotone”:
No sensor has a negative gain
“Submodular”:
Gains follow law of diminishing returns
Size of subset
Accuracy of Localization
Always positive
Reduces with increase in |T|
CDF of std normal
Location means
Cov. matrix of distributions
=
Start with empty subset ,
i.e.
For all available sensors , compute gain and select the one with highest gain
Return selected sensors
Budget reached?
No
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 21: Case of Multiple Locations
“Monotone”:
No sensor has a negative gain
Size of subset
Accuracy of Localization
Always positive
Does not necessarily reduce with increase in |T|
Start with empty subset ,
i.e.
For all available sensors , compute gain and select the one with highest gain
Return selected sensors
Budget reached?
No
Has cross-product of terms,
apart from summation:
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 22: Does Accuracy of Classification Satisfy These Criteria?
Our objective is NOT submodular;
Greedy algorithm does NOT give approximate result
“Monotone”:
No sensor has a negative gain
“Submodular”:
Gains follow law of diminishing returns
Size of subset
Accuracy of Localization
Size of subset
Accuracy of Localization
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 23: Can be Verified using Experiments
Accuracy of Localization
Not submodular due to presence of cross-product terms
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 24: Can we Design an Auxiliary Monotone Submodular Objective?
Accuracy of Localization
(Auxiliary) Greedy algorithm gives near-optimal value of auxiliary objective
Approximate the cross-product terms
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 25: Does it Also Give Guarantee on Performance of Actual Objective?
Applying greedy algorithm on auxiliary objective provides guarantee on accuracy
Analytically show that this difference is within a bound.
Bound reduces with an increase in budget
Accuracy of Localization
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 26: Content
Motivation of Sensor Selection
Problem Formulation
Our Algorithm
Evaluation

## Slide 27: Performance Evaluation Simulation Based on Propagation Models
40 m
40 m
Transmitter at 1600 points; 100 sensors
Landscape based on satellites
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 28: How Does it Compare to State-of-the-art? Large-scale Simulation
Greedy Algorithm
Maximizes the coverage area [Mobicom’ 17]
Select sensors randomly
Auxiliary Greedy Algorithm
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 29: How Does it Compare to State-of-the-art? Large-scale Simulation
Our algorithm provides higher accuracy in practice
Up to 42% higher accuracy than baseline
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 30: Performance Evaluation Indoor Public Dataset
14 m
13 m
Transmitters and sensors at 44 locations
Transmits at 2.4 GHz
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 31: How Does it Compare to State-of-the-art? Indoor Public Dataset
Our algorithm provides higher accuracy in practice
Up to 18% higher accuracy than baseline
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 32: Time Complexity of Our Algorithm
|S| = total number of sensors
B = available budget
Execution Parameters
Execution time
(Not drawn to scale)
m = 1600,
|S| = 100,
B = 20
m = 6400,
|S| = 100,
B = 20
Intel Core i9 processor with 20 cores; nVidia 1080 GTX GPU
10 s
1 min
Does not depend on number of grid cells
Auxiliary Greedy algorithm is fast in practice
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 33: Takeaways
Sensor selection to localize transmitter
Our sensor selection utilizes submodularity
  Utilizes an auxiliary objective
  Evaluations show large improvement in accuracy
  Runs fast over large instances
Our algorithm works better in practice than existing state of the art
  Additional details and dataset at: cs.sunysb.edu/~arbhattachar/specsense