## Slide 1: Towards Performance Guarantees in Emerging Wireless Network Applications
Arani Bhattacharya
Thesis Defense
Stony Brook University

## Slide 2: Number of wireless devices is increasing
All wireless devices utilize spectrum
Access Point
Internet
1) Wireless channel or spectrum getting more busy!
Backhaul
Wired Network
Wireless Devices
Notes: Spectrum scarcity. Cost of spectrum increased from 17 cents/MHz from 2009 to 51 MHz to 2016.

## Slide 3: But Spectrum is a Limited Resource
Spectrum is getting more expensive;
Regulators need to protect it from illegal use
Chart: Median cost Across the world
| 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016
Median $/MHz/Pop | 0.1795 | 0.2247 | 0.2746 | 0.338 | 0.3956 | 0.4411 | 0.5018 | 0.542
Data Courtesy: Effective Spectrum Pricing: Supporting better quality and more affordable mobile services, Full Report, February 2017, Nera Economic Consulting
Increase of 3x in 7 years
Notes: Spectrum scarcity. Cost of spectrum increased from 17 cents/MHz from 2009 to 51 MHz to 2016.

## Slide 4: Need to run applications on devices with weak processors
How can such devices run complex applications?
Access Point
Internet
Backhaul
Wired Network
Wireless Devices
2) Devices are getting smaller and less autonomous
Notes: Spectrum scarcity. Cost of spectrum increased from 17 cents/MHz from 2009 to 51 MHz to 2016.

## Slide 5: Computation offloading can allow running of complex applications
Small devices can offload their compute-intensive tasks to devices with larger processors
Access Point
Internet
Backhaul
Wired Network
Wireless Devices
Small devices offload to cloud
Cloud Server
Notes: Spectrum scarcity. Cost of spectrum increased from 17 cents/MHz from 2009 to 51 MHz to 2016.

## Slide 6: Our Focus is on Two Wireless Applications
Cloud Server
$
$
$
$
1) Regulators need to protect spectrum from illegal use
Spectrum Monitoring
Computation Offloading
Intruder (Unauthorized transmitter)
2) Small devices offload to cloud
Notes: Spectrum scarcity. Cost of spectrum increased from 17 cents/MHz from 2009 to 51 MHz to 2016.

## Slide 7
Introduction and Motivation
Spectrum Monitoring
Computation Offloading to Reduce Execution Time
Conclusion
Content Outline
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 8: How can Regulators Protect Spectrum?
Possible either using one spectrum analyzer or multiple cheap software-defined radios
Illegal transmitters must be detected: 1) With high accuracy
2) At low cost
Intruder (Unauthorized transmitter)
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 9: Two Ways of Monitoring Spectrum
We focus on deploying large number of inexpensive sensors
Large number of inexpensive sensors
Single spectrum analyzer
$50
$1000
Intruder (Unauthorized transmitter)
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 10: Running Many Sensors Incurs Recurring Cost
We reduce recurrent cost while ensuring accurate spectrum monitoring
Intruder (Unauthorized transmitter)
Deployed sensors
Energy consumption and sending data both have monetary cost
Individual sensor decisions need to be processed to get a global decision
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 11: Our Contributions
Offline Sensor
Selection
Online Sensor
Selection
Low-cost Spectrum Monitoring
Fusion of Noisy Sensors
FPGA-based
Sensors
INFOCOM’20
(Under Submission)
INFOCOM’18,
IEEE Tran. Cog. Comm.’ 19
DySPAN’18
To be submitted
Low-cost Spectrum Monitoring
Notes: Spectrum scarcity. Cost of spectrum increased from 17 cents/MHz from 2009 to 51 MHz to 2016.

## Slide 12: “Selection of Sensors for Efficient Transmitter Localization”
Offline Sensor
Selection
Online Sensor
Selection
Low-cost Spectrum Monitoring
Fusion of Noisy Sensors
FPGA-based
Sensors
INFOCOM’20
(Under Submission)
Low-cost Spectrum Monitoring
Notes: Spectrum scarcity. Cost of spectrum increased from 17 cents/MHz from 2009 to 51 MHz to 2016.

## Slide 13: How can we Reduce Cost?
Cost reduction possible by selecting the most relevant sensors
Select sensors
Multiple sensors close to each other may send redundant data
Can we reduce cost without hurting accuracy?
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 14: Problem Setting
Select sensors
Each sensor reports how much power it senses in a particular band
Fusion
Algorithm
Identifies location or presence of intruder
?
Intruder (Unauthorized transmitter)
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 15: Signals are Corrupted by Noise
Stochastic decision problem; multiple sensors can be used to improve the decision
Select sensors
?
Noise Distribution
Signal Distribution
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 16: Maximum a Posteriori Estimate
Provides the optimal accuracy;
shown by R. A. Fisher in 1921
Divide entire area into grid cells
Label each cell as a hypothesis
Compute probability of each hypothesis using Bayes rule
Select maximum
Select sensors
H1
H2
H3
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 17: Which Subset of Sensors Provide Best Accuracy?
Need to solve this optimization problem
Max Accuracy
subject to:
# Sensors ≤ Budget
Select sensors
?
Intruder (Unauthorized transmitter)
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 18: Solving this optimization is NP-Hard
Need to select a good subset fast
Slow execution
No guarantee of accuracy
OR
Select sensors
?
Intruder (Unauthorized transmitter)
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 19: What is the Best or “Optimal” Subset?
Not possible to get quickly because of NP-Hardness
n = Total Number of Available Sensors
B = Number of budgeted sensors
Accuracy of Localization
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 20: Getting "Near-Optimal" Subset
Getting near-optimal subset quickly is possible under "certain" conditions
Smaller the value of , better is the approximation
n = Total Number of Available Sensors
B = Number of budgeted sensors
Accuracy of Localization
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 21: Two Key Conditions on Objective Function
Monotone submodular objectives have approximation results
Size of subset
Accuracy of Localization
Size of subset
Accuracy of Localization
“Monotone”:
No sensor has a negative gain
“Submodular”:
Gains follow law of diminishing returns
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 22: Approximate Result Using “Greedy” Algorithm
“Monotone”:
No sensor has a negative gain
“Submodular”:
Gains follow law of diminishing returns
Size of subset
Accuracy of Localization
Size of subset
Accuracy of Detection
Start with empty subset
For all available sensors, compute gain and select the one with highest gain
Return selected sensors
Budget reached?
Yes
No
Gives a of 1/e
[Nemhauser ‘78]
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 23: Does accuracy of classification satisfy these criteria?
Our objective is NOT submodular;
Greedy algorithm does NOT give approximate result
“Monotone”:
No sensor has a negative gain
“Submodular”:
Gains follow law of diminishing returns
Size of subset
Accuracy of Localization
Size of subset
Accuracy of Localization
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 24: How does Accuracy of Classification Actually Behave?
Only a part of the objective is submodular. Deviates from submodularity on increasing number of hypotheses
Submodular
Accuracy of Localization
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 25: Can we Design an Auxiliary Monotone Submodular Objective?
(Auxiliary) Greedy algorithm gives near-optimal value of auxiliary objective
Accuracy of Localization
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 26: Does it also Give Guarantee on Performance of Actual Objective?
Applying greedy algorithm on auxiliary objective provides guarantee on accuracy
Analytically show that this difference is within a bound.
Bound reduces with an increase in budget
Accuracy of Localization
Accuracy of Localization
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 27: Performance Evaluation Simulation for Large-Scale Experiments
Data generated using Longley-Rice propagation model
Area of 16 sq. km divided into 1600 grid cells
Set of 100 sensors deployed randomly
Repeated 100 times to prove statistical significance
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 28: Comparison with State-of-the-Art Simulation Result
Our algorithm provides higher accuracy in practice
Up to 40% better than coverage
Up to 16% better than basic greedy
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 29: Performance Evaluation Real-data Experiments
Indoor settings:
  Area of 196 sq. m
  44 sensors and transmitters
  Collected in a campus building at University of Utah
Outdoor settings:
  Area of 100 sq. m
  100 transmitters, 18 RTL-SDR based sensors
  Collected in South P Lot
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 30: Comparison with State-of-the-Art Indoor Setting
Our algorithm provides higher accuracy in practice
Up to 16% better than coverage
Up to 5% better than (basic) greedy
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 31: Comparison with State-of-the-Art Outdoor Setting
Our algorithm provides higher accuracy in practice
Up to 15% better than coverage
Up to 12% better than (basic) greedy
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 32: Dealing with Slow Execution
Slow execution
No guarantee of accuracy
OR
Is greedy algorithm fast?
Select sensors
?
Intruder (Unauthorized transmitter)
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 33: Time Complexity of Our Algorithm
Slow execution
??
m = number of hypotheses (grid cells)
|S| = total number of sensors
B = available budget
Execution time
(Not drawn to scale)
40 s
15 min
m = 1600
m = 6400
Intel Core i9 processor with 20 cores; nVidia 1080 GTX GPU
Greedy algorithm is still too slow!
Execution Parameters
|S| = 100, B = 20
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 34: Finding the Bottleneck in Our Algorithm
“Monotone”:
No sensor has a negative gain
“Submodular”:
Gains follow law of diminishing returns
Size of subset
Accuracy of Localization
Size of subset
Accuracy of Detection
Start with empty subset
For all available sensors, compute gain and select the one with highest gain
Return selected sensors
Budget reached?
Yes
No
O(
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 35: Two Key Observations
Time Complexity Reduces to O(|S|B)
Selecting a sensor affects probabilities ONLY within a limited area
  Only iterate over a limited circular area with constant number of hypotheses
Covariance matrix is diagonal
  Using dynamic programming, compute the gain of one sensor in constant time
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 36: Finding the Bottleneck in Our Algorithm
“Monotone”:
No sensor has a negative gain
“Submodular”:
Gains follow law of diminishing returns
Size of subset
Accuracy of Localization
Size of subset
Accuracy of Detection
Start with empty subset
For all available sensors, compute gain and select the one with highest gain
Return selected sensors
Budget reached?
Yes
No
O(|S|)
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 37: Time Complexity of Our Algorithm
Slow execution
m = number of hypotheses (grid cells)
|S| = total number of sensors
B = available budget
Execution Parameters
Execution time
(Not drawn to scale)
40 s
15 min
m = 1600
m = 6400,
Greedy algorithm is now much faster!
10 s
1 min
|S| = 100, B = 20
Intel Core i9 processor with 20 cores; nVidia 1080 GTX GPU
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 38: Performance of Our Algorithm
We guarantee both fast execution and near-optimal accuracy for any given budget
Slow execution
No guarantee of accuracy
OR
Select sensors
?
Intruder (Unauthorized transmitter)
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 39: “Online Selection of Sensors for Transmitter Localization”
Offline Sensor
Selection
Online Sensor
Selection
Low-cost Spectrum Monitoring
Fusion of Noisy Sensors
FPGA-based
Sensors
Low-cost Spectrum Monitoring
To be submitted
Notes: Spectrum scarcity. Cost of spectrum increased from 17 cents/MHz from 2009 to 51 MHz to 2016.

## Slide 40: Online Selection Can Give More Accurate Results
Improves accuracy and reduce cost
Select next sensor after probing a previous sensor
Select sensors
?
Intruder (Unauthorized transmitter)
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 41: Greedy Policy is the Best Strategy
Selecting the best sensor at each step provides a bound with the optimal strategy
“Best” sensor is the one which reduces entropy the most
Select sensors
?
Intruder (Unauthorized transmitter)
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 42: “Quantifying Energy and Latency Improvements of FPGA-Based Sensors for Low-Cost Spectrum Monitoring”
DySPAN’18
Offline Sensor
Selection
Online Sensor
Selection
Low-cost Spectrum Monitoring
Fusion of Noisy Sensors
FPGA-based
Sensors
Low-cost Spectrum Monitoring
Notes: Spectrum scarcity. Cost of spectrum increased from 17 cents/MHz from 2009 to 51 MHz to 2016.

## Slide 43: Benchmark Performance of FPGA-based Spectrum Sensors
FPGA-based spectrum sensors can reduce cost
Raspberry Pi connected to RTL-SDR
FPGA-board with SDR
Android smartphone with RTL-SDR
Latency: x 69
Energy: x 6
Latency: x 73
Energy: x 8
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 44: “Spectrum Patrolling with Crowdsourced Spectrum Sensors”
INFOCOM’18,
IEEE Trans. Cog. Comm’19
Offline Sensor
Selection
Online Sensor
Selection
Low-cost Spectrum Monitoring
Fusion of Noisy Sensors
FPGA-based
Sensors
Low-cost Spectrum Monitoring
Notes: Spectrum scarcity. Cost of spectrum increased from 17 cents/MHz from 2009 to 51 MHz to 2016.

## Slide 45: Sensors May also Send their Local Decisions
?
Fusion
Algorithm
Fusion algorithm needs to get a global decision about the presence of transmitter
Present
Absent
Present
Present
Global Decision | 
Absent
Present
Local Decisions
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 46: We Utilize Local Decisions to get a Global Decision
We weigh the output of each sensor to get the optimal global decision
?
Local Decisions
Present
Absent
Present
Present
Optimal global decision
Fusion
algorithm
Sensor Model (PD, PFA)
Linear combination
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 47: Evaluation of Our Sensor Fusion Algorithm
Our sensor fusion performs better than baseline
Up to 38% improvement in accuracy
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 48: Our Contributions on Spectrum Patrolling
Offline Sensor
Selection
Online Sensor
Selection
Low-cost Spectrum Monitoring
Fusion of Noisy Sensors
FPGA-based
Sensors
INFOCOM’20
(Under Submission)
DySPAN’18
To be submitted
INFOCOM’18,
IEEE Trans. Cog. Comm’19
Notes: Spectrum scarcity. Cost of spectrum increased from 17 cents/MHz from 2009 to 51 MHz to 2016.

## Slide 49
Introduction and Motivation
Low-cost Spectrum Monitoring
Computation Offloading
  Scheduling to Minimize Execution Time
  Satisfying Latency Constraints over Lossy Networks
Summary
Content Outline
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 50
What is Computation Offloading?
Smartphone
met()
gps()
100 ms
50 ms
200 ms
net()
Total = 350 ms
Cloud Server
Smartphone
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 51
Offloading can reduce execution time of applications
What is Computation Offloading?
Cloud Server
Smartphone
Smartphone
met()
gps()
100 ms
50 ms
net()
20 ms
50ms
50ms
Total = 270 ms
Cloud Server
200 ms
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 52
Our Contributions
Cloud Server
Smartphone
Which tasks to offload?
Scheduling tasks to minimize execution time
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 53
Graph partitioning is NP-Hard; can be solved either using an optimization solver or heuristics
Prior Studies use Graph Partitioning
T1
T2
T3
T4
T5
T6
10 ms
10 ms
10 ms
40 ms
10 ms
40 ms
20 ms
30 ms
20 ms
20 ms
20 ms
10 ms
Graph component
Graph component
Graph component
Notes: T4 ends at 30
T3 ends at 58
T5 starts at max(30 + 20, 58 + 2) = 60
T6 starts at 80

## Slide 54
Our technique provides faster execution time
Our Idea
Allow Some Tasks to Execute on Both Platforms
T1
T2
T3
T4
T5
T6
10 ms
10 ms
10 ms
40 ms
10 ms
40 ms
20 ms
30 ms
20 ms
20 ms
20 ms
10 ms
Executed on both phone and cloud
(i.e. duplicate execution)
Notes: T4 -> 30
T5 starts at max(30 + 20, 42) = 50
T5 ends at 52
T6 starts at 72
T6 ends at 82

## Slide 55
Recurrence relation to construct a dynamic programming solution
Dynamic Programming Solution to Minimize Finish Time
T1
T2
T3
T4
T5
T6
10 ms
10 ms
10 ms
40 ms
10 ms
40 ms
20 ms
30 ms
20 ms
20 ms
20 ms
10 ms
Finish time
Execution time
Transmission time
Notes: T4 -> 30
T5 starts at max(30 + 20, 42) = 50
T5 ends at 52
T6 starts at 72
T6 ends at 82

## Slide 56
Our algorithm runs much faster than ILP
Scheduling Time
Name of Benchmark
Notes: T4 -> 30
T5 starts at max(30 + 20, 42) = 50
T5 ends at 52
T6 starts at 72
T6 ends at 82

## Slide 57
We propose a heuristic that satisfies the given constraint while reducing expected finish time
Satisfying Latency Constraint over a Lossy Channel
Cloud Server
Smartphone
Model the number of retransmissions as a Binomial process
Approximate the number of retransmission attempts needed using Hoeffding’s inequality
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 58
Introduction and Motivation
Low-cost Spectrum Monitoring
Computation Offloading to Reduce Execution Time
Summary
Content Outline
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 59
Summary
Offline Sensor
Selection
Online Sensor
Selection
Low-cost Spectrum Monitoring
FPGA-based
Sensors
Low-cost Spectrum Monitoring
Fusion of Noisy Sensors
Algorithm to minimize execution time
Heuristic to satisfy latency constraint
Computation
Offloading
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 60
Arani Bhattacharya, Caitao Zhan, Himanshu Gupta, Samir R Das, Petar M. Djuric; Selection of Sensors for Efficient Transmitter Localization, Under Submission at IEEE Infocom 2020
Arani Bhattacharya, Ayon Chakraborty, Samir R Das, Himanshu Gupta, Petar M. Djuric; Spectrum Patrolling with Crowdsourced Spectrum Sensors, Accepted for Publication at IEEE Transactions on Cognitive Communications and Networking
Arani Bhattacharya, Han Chen, Peter Milder, Samir R. Das, Quantifying Energy and Latency Improvements of FPGA-Based Sensors for Low-Cost Spectrum Monitoring, IEEE DySPAN 2018
Ayon Chakraborty, Arani Bhattacharya, Snigdha Kamal, Samir R Das, Himanshu Gupta, Petar M. Djuric; Spectrum Patrolling with Crowdsourced Spectrum Sensors, IEEE INFOCOM 2018
Publications Part of this Thesis:
Spectrum Monitoring
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 61
Arani Bhattacharya, Ansuman Banerjee, Pradipta De; Scheduling with Task Duplication for Application Offloading, IEEE CCNC 2017
Arani Bhattacharya, Ansuman Banerjee, Pradipta De; Service Level Guarantee for Mobile Application Offloading in Presence of Wireless Channel Errors, IEEE Globecom 2016
Arani Bhattacharya, Pradipta De; Computation offloading from mobile devices: Can edge devices perform better than the cloud?, Third International Workshop on Adaptive Resource Management and Scheduling for Cloud Computing. ACM, 2016
Arani Bhattacharya, Ansuman Banerjee, Pradipta De; Parametric Analysis of Mobile Cloud Computing Frameworks using Simulation Modeling, Second International Workshop on Adaptive Resource Management and Scheduling for Cloud Computing. ACM, 2016
Publications Part of Thesis:
Computation Offloading
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 62
Vasudevan Nagendra, Arani Bhattacharya, Anshul Gandhi, Samir R. Das; Scalable and Resource Efficient Control Plane for Next Generation Cellular Packet Core, ACM Symposium on SDN Research (SOSR) 2019
Sohee Park, Arani Bhattacharya, Zhibo Yang, Mallesham Dasari, Samir R. Das, Dimitris Samaras; Advancing User Quality of Experience in 360-degree Video Streaming, IFIP Networking Conference 2019
Mallesham Dasari, Muhammad Bershgal Atique, Arani Bhattacharya, Samir R. Das; Spectrum Protection from Micro-Transmissions Using Distributed Spectrum Patrolling, Passive and Active Measurement (PAM) 2019
Mallesham Dasari, Santiago Vargas, Arani Bhattacharya, Aruna Balasubramanian, Samir R Das, Michael Ferdman; Impact of device performance on mobile internet QoE, ACM Internet Measurement Conference (IMC) 2018
Sohee Kim Park, Arani Bhattacharya, Mallesham Dasari, Samir R. Das; Understanding User Perceived Video Quality using Multipath TCP over Wireless Network, IEEE Sarnoff Symposium 2018
Arani Bhattacharya, Pradipta De; A Survey of Adaptive Techniques in Computation Offloading, Journal of Network and Computer Applications, 2017
Ayon Chakraborty, Arani Bhattacharya, Santosh Ghosh, Samir R. Das; A first look at performance of TV streaming sticks, IEEE Sarnoff Symposium 2017
Other Related Publications
Notes: No need to discuss the current approach. Also change this spectrum or signal map.

## Slide 63
Summary
Offline Sensor
Selection
Online Sensor
Selection
Low-cost Spectrum Monitoring
FPGA-based
Sensors
Low-cost Spectrum Monitoring
Fusion of Noisy Sensors
Algorithm to minimize execution time
Heuristic to satisfy latency constraint
Computation
Offloading
Notes: No need to discuss the current approach. Also change this spectrum or signal map.